## Slide 1: Identifikation von Varianten durch Berechnung der semantischen Differenz von Modellen
Sylvia Melzer, Ralf God, Thorsten Kiehl,
Ralf Möller, Michael Wessel
Technische Universität Hamburg-Harburg
Institut für Flugzeug-Kabinensysteme, Nesspriel 5, Hamburg
Institut für Softwaresysteme, Schwarzenbergstrasse 95, Hamburg

## Slide 2
Stellen Sie sich vor…
… Sie wollen eine neue Variante eines existierenden komplexen Systems entwickeln.
… Sie wollen bei der Entwicklung einer Variante so viel wie möglich eines Referenzsystems verwenden.
… Sie setzen Methoden und Werkzeuge des Systems-Engineering ein.
… Sie entscheiden sich bei der Entwicklung für ein zukunftsweisendes, modellbasiertes Vorgehen.
Sie wünschten sich…
… es gäbe eine werkzeugtechnische Unterstützung, die Ihnen die Basis (Gemeinsamkeiten) und den variablen Anteil des Referenzsystems automatisch berechnet.
Motivation

## Slide 3
Einleitung
Beispiele für Varianten
Quelle: Lufthansa Cargo
Systemvarianten
Prozessvarianten
Komponentenvarianten
Produktvarianten
Projekt: SiLuFra – Sichere Luftfracht-Transportkette
Modellieren eines Future Gatelink Systems im V-Modell
Projekt: Active Phasing Experiment (APE)
Projekt: SYLVIA – Synergetische Ansätze für neuartige Module, Monumente und Systeme von zukünftigen Flugzeugkabinen
Quelle: http://mbse.gfse.de/extdocs/ape.html
Quelle: [1]
[1]: [Gumpinger, T.; Krause, D.: : Potentiale der Methode Funktionsintegration beim Leichtbau von Flugzeugküchen. Design for X, Beiträge zum 19. Symposium, Neukirchen (2008) pp. 111-118][Jonas, H.; Gumpinger, T.; Blees, C.; Krause, D.: Innovative Design of a Galley Product Platform by applying a new Modularisation Method. 4th International Conference „Supply on the Wings“, Frankfurt/Main (2009)]

## Slide 4
Varianten
Was sind Varianten?
  Variante setzt sich aus einer Basis und einem variablen Anteil zusammen.
Basis
Variabler Anteil
Variante
Basis

## Slide 5
Varianten des
Phasing Wavefront Sensor
Sind die Komponenten ZEUS, DIPSI und SHAPS Varianten?
Quelle: http://mbse.gfse.de/extdocs/ape.html

## Slide 6
Sind die Komponenten ZEUS, DIPSI und SHAPS Varianten?
  Gängige Modellierungstools (z.B. NoMagic Cameo Systems Modeler) unterstützen graphische Differenzen
Varianten
  Varianten lassen sich nicht identifizieren.
Quelle: http://mbse.gfse.de/extdocs/ape.html

## Slide 7
Lösungsansatz
  Berechnung semantischer Differenzen mittels des sogenannten Abox-Differenz-Operators
  Automatische Berechnung der semantischen Differenz durch Einbeziehung einer Wissensbasis (Ontologie) zur Identifikation von Varianten
Frage beantworten:
Sind die Komponenten ZEUS, DIPSI und SHAPS Varianten?
Ontologie
Varianten identifizieren
Quelle: http://mbse.gfse.de/extdocs/ape.html

## Slide 8
Sprache zur Wissensrepräsentation
  Beschreibungslogiken sind eine Familie von Sprachen zur Wissensrepräsentation in Form von Klassen und Beziehungen.
  Verwendung der Beschreibungslogik ALC (Attribute Concept Language with Complement)
  Die Formalisierung der Ontologie lautet: (Tbox, Abox)
Beschreibungslogik
Attribute Concept Language with Complement (ALC)

## Slide 9
Ontologie
Beschreibungslogik zur Repräsentation von Wissen
Tbox
Wissen über Begriffe
(Konzepte und Rollen)
Abox
Wissen über einzelne
Objekte (Instanzen)
„Es gibt eine Instanz zeus vom Konzept ZEUS.“
„ZEUS ist eine Spezialisierung des PhasingWavefrontSensor.“
Ontologie

## Slide 10
Beschreibungslogik zur Repräsentation von Wissen
  Tbox:
  „ZEUS ist eine Spezialisierung des PhasingWavefrontSensor.“
  PhasingWavefrontSensor ≡ isSpecialized.ZEUS
  Abox:
  „Es gibt eine Instanz zeus vom Konzept ZEUS.“
  zeus : ZEUS
Ontologie

## Slide 11
Beschreibungslogik zur Repräsentation von Wissen
Ontologie
Syntax | 
 | Atomares Konzept
 | Atomare Rolle
 | Konjunktion
 | Disjunktion
 | Negation
Syntax | 
 | Atomares Konzept
 | Atomare Rolle
 | Konjunktion
 | Disjunktion
 | Negation
Tbox
Syntax | 
 | Konzeptassertion
 | Rollenassertion
Syntax | 
 | Konzeptassertion
 | Rollenassertion
Abox

## Slide 12
Semantische Differenz der Sensoren ZEUS und SHAPS
Wie unterscheidet sich der Sensor ZEUS vom Sensor SHAPS?
  Antwort liefert die Berechnung der semantischen Differenz beider Sensoren.
  Semantische Differenz:
  Es gibt eine Abbildung φ:inds(SHAPS)inds(ZEUS),
  sodass gilt (, φ(SHAPS)∪∆ZEUS,SHAPS) ZEUS.

## Slide 13
Wie unterscheidet sich der Sensor ZEUS vom Sensor SHAPS?
  φ:inds(SHAPS)inds(ZEUS), (T, φ(SHAPS)∪∆ZEUS,SHAPS) ZEUS
Wie unterscheidet sich der Sensor SHAPS vom Sensor ZEUS?
  φ:inds(ZEUS)inds(SHAPS), (T, φ(ZEUS)∪∆SHAPS,ZEUS) SHAPS
Semantische Differenz der Sensoren ZEUS und SHAPS
ZEUS
SHAPS
∆ZEUS,SHAPS
φ(SHAPS)
T
ZEUS
SHAPS
∆SHAPS,ZEUS
φ(ZEUS)
T

## Slide 14
Sind die Sensoren ZEUS und SHAPS Varianten?
  Es existiert eine Variante ΛZEUS,SHAPS, wenn es eine bijektive Abbildung φ*:inds(φ (SHAPS))inds(φ (ZEUS)) gibt,
  sodass gilt:
  (T, φ*(SHAPS*)∪ ∆φ(ZEUS),φ(SHAPS)) ∆ZEUS,SHAPS
  (T, φ*(ZEUS*)∪ ∆φ(SHAPS),φ(ZEUS)) ∆SHAPS,ZEUS
  φ* ist die Basis
Identifikation der Basis und der variablen Anteile von ZEUS und SHAPS
T
ZEUS
SHAPS
∆ZEUS,SHAPS
φ*
∆SHAPS, ZEUS
Es handelt sich hier um eine vereinfachte Darstellung,
d.h., die Abbildung φ*:inds(φ (SHAPS))inds(φ (ZEUS)) ist bijektiv.

## Slide 15
SysML (Systems Modeling Language) zur Modellrepräsentation
  Jedes SysML-Modell berücksichtigt zwei wesentliche Systemaspekte: die Struktur und das Verhalten eines Systems.
  Die Struktur zeigt Entitäten in einem System und repräsentiert die Beziehungen zwischen ihnen.
  Das Verhalten zeigt, wie sich ein System über die Zeit verhält.
  Hier liegt der Fokus auf der Struktur eines Modells, um Varianten zu identifizieren.
Systems Modeling Language
Quelle: http://mbse.gfse.de/extdocs/ape.html

## Slide 16
Abbildung von SysML auf ALC
Bild 1. Komponenten ZEUS und SHAPS in der Sprache SysML.
Bild 2. Komponenten ZEUS und SHAPS in der Sprache ALC.
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2: Block
(shaps2, bbshaps2): hasLinkTo
shapscover2: Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1: System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
SysML
ALC
Abox
automatisch
Quelle: http://mbse.gfse.de/extdocs/ape.html

## Slide 17
Wie unterscheiden sich die Sensoren ZEUS und SHAPS?
  ZEUS = {(ape1: (APE)), (ape1: (System ⊓ Variation Point)), (zeus1:Physical), (zeus1: PWS), ((ape1,zeus1):zeus), (pws1:PWS), ((pws1,zeus1):hasPart), (breadboard1: Breadboard), (breadboard1: (Mechanics ⊓ Block)), ((zeus1, breadboard1): hasLinkTo), (cover1:Cover), (cover1: (Mechanics ⊓ Block)), ((zeus1, cover1):hasLinkTo), (ccdmount1: CcdMount), (ccdmount1: (Mechanics ⊓ Block)), ((zeus1, ccdmount1):hasLinkTo)}
  SHAPS= {(ape2: (APE)), (ape2: (System ⊓ Variation Point)), (shaps2:Physical), (shaps2: PWS), ((ape2,shaps2):shaps), (pws1:PWS), ((pws1,shaps2):hasPart), (breadboard2: Breadboard), (breadboard2: Block), ((shaps2, breadboard2): hasLinkTo), (cover2:Cover), (cover2: Block), ((shaps2, cover2):hasLinkTo), (shutter2: Shutter), (shutter2: Block), ((shaps2, shutter2):hasLinkTo)}
  Aboxen enthalten technische Konzepte wie z.B. Cover und Shutter.
Aboxen ZEUS und SHAPS
Abox

## Slide 18
Berechnung der semantischen Differenz
  ∆ZEUS, SHAPS = {((ape1,zeus1):zeus), (bbzeus1: (Breadboard ⊓ Mechanics ⊓ Block)), (zeuscover1: Cover ⊓ Mechanics ⊓ Block)), (ccdm1: (CcdMount ⊓ Mechanics ⊓ Block))}
  ∆SHAPS, ZEUS = {(ape2,shaps2):shaps, (shutter2: Shutter ⊓ Block)}
Semantische Differenzen der Sensoren ZEUS und SHAPS
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2: Block
(shaps2, bbshaps2): hasLinkTo
shapscover2: Block
(shaps, shapsCover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS
∆SHAPS, ZEUS
Notes:   Die semantischen Differenzen ∆A,B und ∆B,A unterscheiden sich, weil die Blöcke in SHAPS nur den Stereotypen <<block>> besitzen. Wenn der Stereotyp <<Mechanics>> bei der Modellierung der SHAPS-Komponentenblöcke vergessen wurde, kann die Ergebnismenge der semantischen Differenz hilfreich sein, Hinweise auf eine vollständige Modellierung zu liefern.

## Slide 19
Berechnung der semantischen Differenz
  Ergänzung der Abox SHAPS um den Stereotypen <<Mechanics>>
  SHAPS* = {(ape2: (APE)), (ape2: (System ⊓ Variation Point)), (shaps2:Physical), (shaps2: PWS), ((ape2,shaps2):shaps), (pws1:PWS), ((pws1,shaps2):hasPart), (bbshaps2: Breadboard), (bbshaps2: Mechanics ⊓ Block), ((shaps2, bbshaps2): hasLinkTo), (cover2:Cover), (cover2: Mechanics ⊓ Block), ((shaps2, shapscover2):hasLinkTo), (shutter2: Shutter), (shutter2: Mechanics ⊓ Block), ((shaps2, shutter2):hasLinkTo)}
  ∆ZEUS, SHAPS* = {((ape1,zeus1):zeus), (ccdm1: (CcdMount ⊓ Mechanics ⊓ Block))}
  ∆SHAPS*, ZEUS = {(ape2,shaps2):shaps, (shutter2: Shutter ⊓ Mechanics⊓ Block)}
Semantische Differenzen
von ZEUS und SHAPS*

## Slide 20
Berechnung der semantischen Differenz
Semantische Differenzen
von ZEUS und SHAPS*
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS
∆SHAPS, ZEUS
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Mechanics Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Mechanics Block
(shaps, shapscover): hasLinkTo
shutter2:
Mechanics Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS*
∆SHAPS*, ZEUS
⊓
⊓
⊓

## Slide 21
Berechnung der Varianten
  ΛZEUS,SHAPS* = Basis ∪ ∆ZEUS, SHAPS*
  ΛSHAPS*,ZEUS = Basis ∪ ∆SHAPS*, ZEUS
  mit Basis = φ*(SHAPS**) = φ*(ZEUS*)
  Basis = {(ape: (APE)),
  (ape: (System ⊓ Variation Point)), (sensor:Physical),
  (sensor: PWS), (pws:PWS), ((pws,sensor):hasPart),
  ((sensor, breadboard): hasLinkTo),
  ((sensor, cover):hasLinkTo),
  (breadboard: (Block⊓ Mechanics)),
  (cover: (Block ⊓ Mechanics))}
Basis und variable Anteile von
ZEUS und SHAPS*

## Slide 22
Berechnung der Varianten
  ΛZEUS,SHAPS* = Basis ∪ ∆ZEUS, SHAPS*
sensor: Physical
breadboard:
Mechanics Block
(sensor, breadboard): hasLinkTo
cover:
Mechanics Block
(sensor, cover): hasLinkTo
ccdm1:
Mechanics Block
(sensor, ccdm1):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
⊓
⊓
⊓
pws: PWS
(pws1, sensor):
hasPart
⊓
Basis und variable Anteile von
ZEUS und SHAPS*

## Slide 23
Berechnung der Varianten
  ΛSHAPS*,ZEUS = Basis ∪ ∆SHAPS*,ZEUS
sensor: Physical
breadboard:
Mechanics Block
(sensor, breadboard): hasLinkTo
cover:
Mechanics Block
(sensor, cover): hasLinkTo
shutter2: Block
(sensor, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, shaps2): shaps
⊓
pws: PWS
(pws1, sensor):
hasPart
⊓
⊓
Basis und variable Anteile von
ZEUS und SHAPS*

## Slide 24
Berechnung der Varianten
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Mechanics Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Mechanics Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS*
∆SHAPS*, ZEUS
⊓
⊓
Basis
Basis und variable Anteile von
ZEUS und SHAPS*

## Slide 25
Berechnung der semantischen Differenz
  Individuennamen von SHAPS und DIPSI unterscheiden sich
  DIPSI = {(ape3: (APE)), (ape3: (System ⊓ Variation Point)), (dipsi3:Physical), (dipsi3: PWS), ((ape3, dipsi3): dipsi), (pws1:PWS), ((pws1, dipsi3):hasPart), (breadboard3: Breadboard), (breadboard3: Block), ((dipsi3, breadboard3): hasLinkTo), (cover3:Cover), (cover3: Block), ((dipsi3, cover3):hasLinkTo), (shutter3: Shutter), (shutter3: Block), ((dipsi3, shutter3):hasLinkTo)}
  ∆SHAPS,DIPSI = {(ape2, shaps2): shaps}
  ∆DIPSI,SHAPS = {(ape3, dipsi3): dipsi}
Semantische Differenzen
von SHAPS und DIPSI

## Slide 26
Berechnung der Varianten
  ΛSHAPS,DIPSI = Basis ∪ ∆SHAPS,DIPSI
  ΛDIPSI,SHAPS = Basis ∪ ∆DIPSI, SHAPS
  Basis = {(ape: (APE)), (ape: (System ⊓ Variation Point)),
  (sensor:Physical), (sensor: PWS),
  (pws:PWS), ((pws, sensor):hasPart),
  (breadboard: Breadboard),
  (breadboard: Block),
  ((sensor, breadboard): hasLinkTo),
  (cover:Cover), (cover: Block),
  ((sensor, cover):hasLinkTo),
  (shutter: Shutter), (shutter: Block),
  ((sensor, shutter):hasLinkTo)}.
Basis und variable Anteile von
SHAPS und DIPSI
breadboard: Block
(sensor, breadboard): hasLinkTo
cover: Block
(sensor, cover): hasLinkTo
shutter: Block
(sensor, shutter):
hasLinkTo
apei:
System Variation point
⊓
pws1: Block
(pws1, sensor):
hasPart
sensor: Physical

## Slide 27
Berechnung der semantischen Differenz
  Cover wird beim SHAPS-Sensor (Abox SHAPS*) durch einen speziellen ShapsCover ersetzt.
  Die Tbox lautet: T={shapsCover ⊑ Cover}.
  SHAPS** = {(ape2: (APE)), (ape2: (System ⊓ Variation Point)), (shaps2:Physical), (shaps2: PWS), ((ape2,shaps2):shaps), (pws1:PWS), ((pws1,shaps2):hasPart), (bbshaps2: Breadboard), (bbshaps2: Block), ((shaps2, bbshaps2): hasLinkTo), (shapscover2:ShapsCover), (shapscover2: Block), ((shaps2, shapscover2):hasLinkTo), (shutter2: Shutter), (shutter2: Block), ((shaps2, shutter2):hasLinkTo)}
Definition einer Tbox und der Abox SHAPS**
Tbox

## Slide 28
Berechnung der semantischen Differenz
  ∆ZEUS, SHAPS** = {((ape1,zeus1):zeus),(ccdm1: (CcdMount ⊓ Mechanics ⊓ Block))}
  ∆SHAPS**, ZEUS = {(ape2,shaps2):shaps, (shutter2: Shutter ⊓ Mechanics ⊓ Block), (cover2: ShapsCover ⊓ Mechanics ⊓ Block}
Semantische Differenz von
ZEUS und SHAPS**

## Slide 29
Berechnung der semantischen Differenz
  T = {shapsCover ⊑ Cover}
Semantische Differenz von
ZEUS und SHAPS**
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Mechanics Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Mechanics Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS*
∆SHAPS*, ZEUS
⊓
⊓
Basis
⊓
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Mechanics Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Mechanics Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS**
∆SHAPS**, ZEUS
⊓
⊓
Basis
Cover
shapsCover
⊓
Tbox

## Slide 30
Diskussion
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2: Block
(shaps2, bbshaps2): hasLinkTo
shapscover2: Block
(shaps, shapsCover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS
∆SHAPS, ZEUS
zeus1: Physical
bbzeus1:
Mechanics Block
(zeus1, bbzeus1): hasLinkTo
zeuscover1:
Mechanics Block
(zeus1, zeuscover1): hasLinkTo
ccdm1:
Mechanics Block
(zeus1, ccdm1):
hasLinkTo
shaps2: Physical
bbshaps2:
Mechanics Block
(shaps2, bbshaps2): hasLinkTo
shapscover2:
Mechanics Block
(shaps, shapscover): hasLinkTo
shutter2: Block
(shaps2, shutter2):
hasLinkTo
ape1:
System Variation point
(ape1, zeus1): zeus
(ape1, shaps2): shaps
⊓
⊓
pws1: Block
(pws1, zeus1):
hasPart
(pws1, shaps2):
hasPart
⊓
∆ZEUS, SHAPS**
∆SHAPS**, ZEUS
⊓
⊓
Basis
Cover
shapsCover
T={shapsCover ⊑ Cover}
breadboard: Block
(sensor, breadboard): hasLinkTo
cover: Block
(sensor, cover): hasLinkTo
shutter: Block
(sensor, shutter):
hasLinkTo
apei:
System Variation point
⊓
pws1: Block
(pws1, sensor):
hasPart
sensor: Physical
Identifikation von Varianten

## Slide 31
Sie können nun…
… eine neue Variante eines existierenden komplexen Systems entwickeln.
… so viel wie möglich eines Referenzproduktes bei der Entwicklung einer Variante verwenden.
… Methoden und Werkzeuge des Systems-Engineering einsetzen.
… sich für eine zukunftsweisendes, modellbasiertes Vorgehen bei der Entwicklung einer Variante entscheiden.
Denn…
… mit dem Abox-Differenz-Operator können Sie automatisch semantische Differenzen berechnen, um die Basis vom variablen Anteil eines komplexen Systems abzugrenzen.
Zusammenfassung

## Slide 32
  Vielen Dank!
  Fragen?